## Slide 1: AME 480/580 Introduction to nuclear engineering
Neutron distribution in energy
2/2/18

## Slide 2: references
Lewis

## Slide 3: Ch-3: neutron distributions in energy
We introduced the concept of multiplication factor, .
The value of multiplication factor essentially depends on neutron interactions.
Neutron interactions depend on several factors…neutron energy being the primary factor.
For neutrons to interact, we need something to interact with. Another factor is target material composition.
We talk a little more about neutron energetics and important target material properties in this Ch.
We make two main assumptions
  Neutrons are produced instantaneously (in reactors there are two neutron sources – fission neutrons and neutrons from decay of fission products. Fission neutrons are produced instantaneously but neutrons from decay according to characteristic decay constant…in this chapter we consider case with only instantaneously produced neutrons…we will expand our study to incorporate delayed neutrons in a later chapter)
  Spatial effects are integrated out and don’t need to consider them…we defer study of spatial effects to the second half of this course
We go by the book here… we talk about:
  Properties of nuclear fuel and moderator material
  Energy distribution of neutrons in reactors – more details on fast, slowing down, thermal neutrons
  Averaging of neutron cross-section over energy
  Neutron multiplication in terms of energy-averaged cross-sections

## Slide 4: Ch-3 tentative schedule
Monday
  Fast neutrons
  Neutron Slowing down
  Energy self-shielding
  Thermal neutrons
  Reactor spectra
Wednesday
  Energy averaged reactor rates
  Fast cross section averages
  Resonance cross section averages
  Thermal cross section averages
  Infinite medium multiplication
Friday
  Leftovers
  Recap
  HW-2 Solution
Today
  Intro
  Nuclear fuel properties
  Neutron moderators
  Balance equation for neutrons in energy
  Multiphysics intro

## Slide 5: Nuclear fuel properties - basics
We saw in the last chapters that xs depend on energy.
Much of the physics of nuclear reactors is determined by the energy dependence of cross-sections of fissile and fertile materials over the range of incident neutron energies.
Again neutron energies range between fission spectrum and Maxwell-Boltzmann distribution for thermal neutrons – roughly between 10 MeV and 0.001 eV.
Fissile materials have significant fission cross-sections over the entire energy range.
In contrast, fission is possible for fertile materials only if incident neutrons have energy above a certain threshold (for example for U-238 it is ~ 1 MeV)
Not all of the absorbed neutrons cause fission. Some fraction will simply be captured.
The fraction that fissions is also energy dependent.
Number of fission neutrons produced per neutron absorbed plays an important role in reactor’s neutron economy:
is the number of neutrons produced per fission and .

## Slide 6: Neutron fuel properties - basics
To sustain a chain reaction, the average value of neutron economy () must be substantially higher than 1 as in reactors, neutrons will be lost to absorption in structural, coolant, and other materials, and some will leak out of the system.
To examine behavior of let us first consider single fission isotope.
Neutron economy equation can be rewritten as by cancelling number densities in numerator and denominator.
Given this new definition, we can plot neutron economies for U-235 and Pu-239 over energy (see figures on right).
Clearly if we are going to keep greater than one to sustain a chain reaction, we must avoid neutron energy roughly between 1 eV and 0.1 MeV because values drop significantly below one.
Therefore, reactors primarily operate in either thermal range or in fast range but not in epithermal range.

## Slide 7: Nuclear economy for mixtures
Most reactors don’t use pure fissile or predominately fissile materials as fuel.
Except for naval propulsion systems designed for the military, and nukes we try to design our systems with natural U or low-enriched fuel due to proliferation risks and enrichment costs (obviously for something so complicated, Chuck Norris would have to be called and his wages are too high.)
Therefore, reactor fuels consist primarily of U-238 with a smaller fraction of fissile material (U-235).
Depending on design most civilian reactors consist of U with enrichment ranging from 0.7 % to 20 % of fissile material.
We defined enrichment for U in previous classes. We analogously define enrichment for the general case as where and denote fertile and fissile respectively.
In order to find the neutron economy then, where and are now composite xs for the fissile-fertile mixture.
Homework: Look up US-Russia Highly Enriched Uranium Purchase Agreement. Summarize your findings. What are your views on the deal?

## Slide 8: Nuclear fuel properties - implications
The figure to the right plots for natural (0.7%) and 20% enriched U.
Note how suddenly valleys below 1 as a result of resonance capture in U-238 in the epithermal range.
Above threshold of 1 MeV, increasing fission xs of U-238 greatly aids increasing value of .
The curves emphasize why power reactors are fast or thermal but not epithermal….because they want to avoid them valleys in
Fast reactor cores:
  Material other then fuel eliminated in core design
  They want to avoid collisions that cause neutrons to lose energy – elastic scattering with low atomic weight…
  They want to minimize loss of energy due to inelastic scattering with fertile material as well…so they cut the proportion of fertile material in fuel
  Typically for fast reactors, fuel is enriched to 10% or more.
Thermal reactor cores:
  Neutrons must be slowed down to thermal range while avoiding epithermal range as much as possible.
  We must work to slow neutrons down past the “neutron death valley” to the promised land where and there are rainbows and unicorns.
  This mean we want high amount of elastic scattering with low atomic weight materials called moderators.
  For optimized moderator to fuel ratio, reactors can be designed for much lower enrichment. For example CANadians DO CANDU with natural U and moderator.

## Slide 9: neutron moderator
Moderators are important for thermal reactors.
They are required to reduce neutron energies from fission spectrum to thermal range with as few collisions as possible which by passing death valley for neutrons in U-238.
We know that neutron slowing down is modeled through neutron slowing down density which depends heavily on collision parameter.
To be an effective moderator, material must have low A as only then is large enough to slow neutrons down to thermal energies with relatively few collisions.
Other than having a low atomic weight, moderators must also have a high scattering cross-section. I mean if the neutron collides with a light nucleus only to get captured, then it is killing the chain reaction right there right?
Therefore a second parameter in determining material’s value as a moderator is the slowing down power, defined as .
Note here that we have number density as a part of slowing down power. Therefore, the material should be dense enough to be effective. For example, He has a good slowing down decrement and scattering cross-section but it is a bad moderator since it is a gas and has low density.
At the same time, He is a good material to cool fast reactors down as it does not degrade neutron energy spectrum.
Slowing down decrement is the mean value of log of energy loss ratio:
Collision parameter:
Number of collisions to slow down from to :

## Slide 10: Slowing down ratio
Slowing down ratio is the ratio of slowing down power to thermal absorption xs:
The better the absorption ratio, the better the moderator - is by far the best moderator by that standard and allows to build reactors with natural U without any enrichment.
Low slowing down power of graphite makes it a difficult undertaking to build reactors that are graphite moderated (however there exist some designs that are graphite moderated).
Higher thermal absorption in light water requires fuel to be enriched somewhat.
Large thermal absorption eliminates several other materials e.g. boron. B however is used as a poison to control or shutdown chain reactions.
Later in the course once we know how to do diffusion, we will try to write a code to see how increasing concentration of B in reactors affects reactor power over time….remind me at that time if I forget.

## Slide 11: Neutron energy spectra
The distribution of neutrons in energy is determined by competition between scattering and absorption.
Again, for neutrons with energies significantly higher than thermal range, scattering results in degradation of the neutron energy.
For neutrons with energy in thermal range, scattering could result in gain or loss of energy with nearly equal probability due to thermal motion of nuclei.
For medium for which the average energy loss per collision and ratio of scattering to absorption xs are both large, the neutron distribution in energy is will be close to thermal equilibrium – this is thermal or soft spectrum.
For medium in which ratio of neutron scattering to absorption, neutrons are absorbed before significant slowing down takes place. This distribution lies closer to fission spectrum and is said to be fast or hard spectrum.

## Slide 12: NEUTRON ENERGY BALANCE IN ENERGY
Neutron distribution may be expressed in terms of neutron density:
Such that
We define neutron flux as
Here, is the velocity corresponding to kinetic energy E.
Flux is often called scalar flux (as we also have an angular flux in transport which we may or may not talk about later in the course). We interpret as the total distance traveled during one second by all neutrons with energies between and located in unit volume.
The cross-section is interpreted as
Now multiply flux and xs:

## Slide 13: NEUTRON ENERGY BALANCE IN ENERGY continued
If we integrate over all energy, we obtain
To get a more quantitative understanding of neutron energy distribution, we write down a balance equation in terms of neutron flux.
We consider steady state balance  rate of neutron loss = rate of neutron gain
Neutron loss  As neutrons collide they are removed from energy E.
  Collision rate per cc for neutrons of energy E is therefore, rate of loss is
Neutron gain  Gains come from fission and scatter into energy E.
  Fission neutrons are born according to fission spectrum . If we let to be the rate of fission neutron production per cc, is the rate of neutron gain at energy E due to fission.
  Neutrons scatter to energy E from energy between E’ and E’+dE with a probability . Moreover, number of neutrons scattered from energy E’ is . Then the number of neutrons scattering in to energy E from all different energies E’ can be calculated as:
The neutron balance equation in energy then is:

## Slide 14: MULTIPHYSICS PROBLEM INTRODUCTION
See PDF