## Slide 1: AME 480/580 Introduction to nuclear engineering
Neutron slowing down density and cross-section averaging
2/5/18

## Slide 2: First things first Extra credit final project - rough description
We will expand upon the model I have in that paper I shared the other day.
We will do the following:
  Nondimensionalize the problem
  Swap out temperature equation for heat diffusion equation
  Incorporate temperature correction into our model (so with changing temperature our cross-section changes)
  Other things stay the same more or less
  We will also try different methods of coupling – IMEX, Picard, JFNK, NKA (not all obviously but lets see what we can get done)
I will make you guys do smaller problems before we do the big problem so don’t be sacred. This is only extra credit. You’ve got nothing to lose but if you do this…it may be very useful for you in future. Give it a shot…or not…no one is judging you here…we are all learning…I’m learning too (to communicate better and give lectures that you guys find useful and not boring) 
Do we meet separately or do I do some of this in class on Fridays or during office hours? I’m not sure yet.
Having said that, I ask you to solve Bateman equation numerically for your midterm exam. It will be a small problem though so that you can compare your solution to analytical answer that we already derived so that you get a taste of how to do that. 😈

## Slide 3: references
Lewis

## Slide 4: Last time on “bubba does reactors”
We saw in Ch. 1 where nuclear energy comes from.
  Therefore, given average number of reactions in a reactor, we can estimate the thermal power a reactor might produce.
In Ch. 2 we looked at the likelihood of specific reactions happening.
  We looked at cross-sections and composite cross-sections for specific reactions like scattering and fission
We started Ch. 3 last time
  We began to explore energy dependence of fission cross sections in some detail.
  We saw that reactors can only be build for neutrons in either fast or thermal range but not epithermal range
  If we build a reactor for fast range, we must avoid scattering collisions that cause neutrons to slow down past the fast energy range…we avoid light nuclei in and around core.
  If we build a reactor for thermal range, we must slow neutrons down from fast to thermal neutron energy range.
    We must do it, however, in such a way that we don’t lose neutrons to resonance capture in the epithermal range.
    To do that we use “moderators” that allow neutrons to slow down from fast range to thermal range bypassing the neutron valleys of death in epithermal range as much as possible.

## Slide 5: Last time – fuel
We realized that fuel is almost never made up of purely fissile material. It comes bundled with fertile material in nature.
Enrichment is expensive. Moreover it is also a nonproliferation risk. So barring nuclear submarines and nuclear weapons, most nuclear systems are powered by either natural U or low enriched U (~0.7%-20%)
Moreover, we noted that neutrons could be lost to absorption in
Therefore, in order to characterize efficiency of fuel, we introduced neutron economy:
where, = average # neutrons produced per fission; = enrichment of fuel; = fission xs for fissile material for a neutron of energy E; = absorption cross-section for fertile material and so on…
Shape of tells us why we build reactors for thermal or fast neutrons

## Slide 6: Last time – moderator
Moderator needed for thermal reactors to slow neutrons from fast range (fission spectrum) to thermal range (Maxwell-Boltzmann distribution) while bypassing resonance capture (neutron valley of death).
A moderator must have the following characteristics (collide, scatter, don’t get absorbed, lose a lot of energy per scatter so that they don’t get caught in resonances):
  High density – why? Cuz we want neutrons to collide with nuclei (high density means higher number of nuclei for neutrons to collide with)
  High scattering cross-section – why? Cuz we actually want neutrons to scatter after they collide with nuclei
  Low absorption cross-section – cuz we don’t want to lose neutrons to the moderator (we want them to be absorbed in fuel)
  Low atomic number – Low atomic number nuclei allow neutrons to scatter down to thermal region with low number of scatters…if neutrons lose a large amount of energy per collision, then they are more likely to jump resonances and not get stuck in them.
Three parameters quantify quality of moderator:
  Slowing down decrement - ; ;
  Slowing down power -
  Slowing down ratio -
Heavy water best moderator because it has best slowing down ratio and can be used with natural U to build reactors….boron best poison to control chain reaction

## Slide 7: Last time – neutron balance
= macroscopic cross-section = probability that a neutron will undergo a reaction per unit distance
= total distance traveled by all neutrons with energy between E and E+dE per unit time in unit volume
So then if you multiply the above two
= total number of collisions by neutrons of energy E per unit time in unit volume
When we integrate over energy,
= number of reactions per second by all neutrons in unit volume …. Keep that in mind!
Balance: NEUTRON LOSS = NEUTRON GAIN
NEUTRON GAIN – Neutrons are removed from E as they collide
NEUTRON LOSS – Neutrons are either born to fission at E or they scatter up/down to E
= rate of fission neutron production per cc
Then the number of neutrons scattering in to energy E from all different energies E’ can be calculated as

## Slide 8: bubba does reactors – season 3 episode 2
Bubba learns to quantify neutron scalar flux as a function of energy.
***Intro Music***
BLACKBOARD 