## Slide 1: AME 480/580 Introduction to nuclear engineering
Nuclear reactions
1/17/18

## Slide 2: references
  Fundamentals of Nuclear Reactor Physics by E. E. Lewis
  Introduction to Nuclear Engineering by J. R. Lamarsh and A. J. Baratta
  http://www.atomicarchive.com/Fission/Fission2.shtml
  https://en.wikipedia.org/wiki/Stable_nuclide

## Slide 3: Outline
Energy conservation
Binding Energy
Fusion Reactions
Fission Reactions

## Slide 4: Energy Conservation
Consider a reaction:
Energy conservation states that the overall total energy of interacting particles before and after the reaction are the same.
Recall that total energy is the sum of kinetic energy and rest-mass energy:
Then energy conservation for the above nuclear reaction is written as:
Recall that , substituting that in the above relation, we have:
Rearranging the above equation returns:
The difference in rest mass energies of nuclei before and after the reaction is called the Q value of the reaction. This value determines whether the reaction is exothermic or endothermic.

## Slide 5: Energy Conservation - continued
Question: What is the difference between exothermic and endothermic? What does our reaction need to be in order to produce power?
A positive Q value indicates exothermic reaction. This creates kinetic energy and results in net loss of rest mass energy.
Endothermic reactions result in increase in rest mass energy.
This is the same as with chemical reactions except, with nuclear reactions, energy changes are of the order of MeV (compared to eV for chemical reactions – so that is six orders of magnitude difference).
  See why nuclear power is much more efficient and requires much less fuel to generate power?
Homework (10 points): Write down conservation laws and calculate the Q value for the following reaction. Also determine whether the reaction is exothermic or endothermic.

## Slide 6: Binding energy
In order to know a-priori which reactions will be exothermic and which reactions will be endothermic we need to examine the ideas of binding energy and mass defect.
Mass Defect: Any nuclide has Z protons and A-Z neutrons. If we weigh protons and neutrons separately, sum the masses up and compare it to the mass of nuclide X, we find that weights of the constituent particles is higher than that of the nucleus as a whole (for all nuclei). This difference is called mass defect:
Binding Energy: The energy equivalent of mass defect is the energy that binds neutrons and protons together in the nucleus. In other words, in order to pull a nucleus apart into its constituent particles, we would need to expend this amount of energy. This energy equivalent is called binding energy:
Binding Energy per Nucleon: Just as the name suggests, we normalize the binding energy to the number of nucleons to get binding energy per nucleon:
Homework (10 points): Calculate binding energy per nucleon for U-235 and U-238.

## Slide 7: Binding energy continued
Binding energy per nucleon provides “a” measure of stability of nucleus. In general, the higher the value, the more stable the nucleus will be. It is not a rule, however.
Exothermic reactions are those in which daughter nuclei have a higher binding energy than parent nuclei. Therefore in exothermic reactions, we go from less to more stable nuclei.
Two classes of such exothermic reactions become important for energy production:
Fusion: Two light nuclei “fuse” to form a heavier nucleus – higher on the binding energy curve.
Fission: A heavy nucleus splits into lighter nuclei, each with higher binding energy per nucleon.
This makes sense if you look at the curve – we go from light nuclei to heavy nuclei via fusion – binding energy per nucleon increases – exothermic reaction….or…we go from heavy nuclei to lighter nuclei via fission – again binding energy per nucleon increases – exothermic reaction – energy production.

## Slide 8: Fusion reaction
Fusion reactions under consideration are based on fusing isotopes of hydrogen:
  Deuterium-Deuterium (D-D):
  Deuterium-Tritium (D-T):
So how do you attain fusion exactly?
Nuclei have protons and protons repel each other. In order to overcome this repulsion between charged nuclei, they must collide at very high speeds and overpower Coulombic repulsion. This can be done in one of the following two ways:
  Use particle accelerators to impart kinetic energy to relevant particles/nuclei and then slam them into target nuclei that make up the second material.
  Mix the two fusing species and bring them to very high temperatures where they become plasma. Average kinetic energy is proportional to the temperature (according to Maxwellian distribution...next slide).
    At high enough temperatures, nuclei attain sufficient kinetic energy to overcome Coulombic repulsion. Such reactions where external heating is involved are called thermonuclear reactions.

## Slide 9: Maxwellian distribution for kinetic energy of particles
In a gas, energies of atoms are distributed according to the Maxwellian function.
Let N(E) be the particle density per unit energy then N(E)dE is the number of particles per unit volume between energy E and E+dE.
According to the Maxwellian distribution,
Here, k is the Boltzmann constant and T is the temperature. The above formula applies for solids, liquids and gases upto 300K. Beyond that temperature, the above formula will slightly differ from the one stated for solids and liquids.
is the most probable energy and is the energy corresponding to the maximum of the curve.
is the average energy

## Slide 10: Is fusion practical?
As seen before, in order to attain fusion, we must overcome Coulombic repulsion between relevant nuclei.
Doing this requires energy. It is not practically possible using accelerators since accelerators use up much more energy than fusion reactions that they facilitate.
So we are left with only one option – raise the temperature and go the plasma route. This means we must produce temperatures comparable to those found in the interior of the Sun.
Long-term efforts continue to achieve controlled temperatures high enough to obtain thermonuclear fusion. More emphasis is placed on D-T reactions because it is feasible at lower temperatures.
The disadvantage of D-T reactions is that most energy release with them comes in the form of KE of neutrons (~14MeV) and they damage the material they impact and make that material radioactive.
Homework (10 points): Look up thermonuclear fusion. Summarize your findings.
Extra credit (5 points): Look up cold fusion. Summarize your views.

## Slide 11: Fission reactions
Since fusion reactions are so wonderfully practical and not hard to achieve at all, we will not care about them any further in this class. Let’s take a look at fission now.
Consider fission of U-235. A neutron hits U-235, nucleus becomes something called a “compound” nucleus which is unstable. The compound nucleus breaks giving out two to three neutrons, lighter nuclei (called fission fragments), gamma rays and neutrinos, plus energy (~200 MeV) in the form of KE of these fission products.
Fission of U-235:

## Slide 12: Fission energy release and dissipation
~200 MeV of energy is released by fission as KE of fission fragments, neutrons, and gamma rays.
Fission fragments further undergo radioactive decay to produce beta rays, gamma rays and neutrinos.
Fission Fragments: Highly charged! High speed fission fragments that emerge from fission cause electrons to be ripped from surrounding atoms (ionization). They lose energy by causing ionization, slow down, and eventually come to rest. Positive ions and free electrons eventually reunite to form neutral atoms while releasing heat. The range in which such heat generation occurs is few microns. More than 80% energy released as KE of fission fragments.
Neutrons: Neutrons are neutral. They behave differently than fission fragments. They travel in straight lines until they collide with nuclei to scatter or get absorbed. If they get absorbed they cease to exist. If they scatter they change energy and direction and continue moving along another straight-line path. Flight path is much larger than interatomic distances. Except at very low energy, they impart significant KE to nuclei causing it to be stripped of electrons and therefore charged. Upon collision they lose energy, decelerate and eventually come to rest .
Neutrinos: Neutrinos, like neutrons do not have a charge. Therefore they travel in straight lines also. However, the flight path for neutrinos is near infinity.
  Now let us think about…how do we “cleverly” use this property of neutrinos?
  Neutrinos come from decay of fission fragments.
  Fission implies reactor/weapon….so depending on neutrino signature, we can determine what kind of nuclear system is at play.

## Slide 13: Biological hazards of radiation
Neutral and charged particles dissipate energy by different mechanisms.
Therefore, they cause different biological hazards.
Alpha and beta are charged particles that deposit energy over very short range. They do not penetrate skin so if the source is external they will not cause much damage. However, if you happen to inhale or ingest the source, somehow, it could potentially be fatal.
If they are inhaled or ingested, they attack lungs or digestive tract…they may affect other organs as well depending on the biochemical properties of the radioisotope inhaled. Eg. Radiostrontium deposits in bone marrow while radioiodine deposits in thyroid gland.
Neutral particles have a larger range – travel further in the body – a few cm. They are an external hazard. Damage from neutral particles is distributed over the entire body due to ionization of water and tissue molecules where neutrons collide with nuclei and gamma particles with electrons.

## Slide 14: Neutron Multiplication
As a neutron travels and interacts with ambient material – they either scatter or get absorbed. If they absorb, and conditions are conducive to fission (and we will talk about what “conducive” means in the next chapter), we see fission.
If each fission, then produces more neutrons, these new neutrons further interact with ambient material and cause further fission in the material and so on. This is the fission chain reaction. This is the idea nuclear reactors operate on.
We characterize this chain reaction by defining a multiplication factor, k.
The multiplication factor is essentially the ratio of number of fission neutrons born in one generation to that in the preceding generation:

## Slide 15: Preliminary math on
Let the number of neutrons in a system at t=0 be
The number of neutrons in the next generation is
Now, 
Assuming the multiplication factor stays constant over time, the second generation will have …generalizing this result to generation, we have,
Note that our relation is in terms of generation number which is not necessarily useful. We want to have this relation as a function of time now. What do we do?
First we define a neutron lifetime, , as average time from birth (through fission), aging (slowing down due to scattering) and death (absorption) for neutrons.
Then, on an average, the time at which the generation is born is and the number of neutrons present in the system at time, , is

## Slide 16: Neutron multiplication continued
The neutron population will increase, decrease or remain the same depending on the value of k.
If k > 1  supercritical; k < 1  subcritical; k = 1  critical
Now let us consider multiplication behavior when k ~ 1.
In order to do that, let us recall relations between exponential function and a logarithm (inverse functions):
; ; so .
Now apply these relations to
Now note that we want to evaluate the value of when . In order to do that, expand in Taylor series around 1:
Keeping the first term and ignoring higher order terms (why can you do that?), we find that
Then,
Therefore, neutrons show exponential growth/decay. The idea of multiplication will be studied at length later on.