## Slide 1: AME 480/580 Introduction to nuclear engineering
Neutron interactions
1/26/18

## Slide 2: references
Lewis
Duderstadt and Hamilton
Baratta and Lamarsh

## Slide 3: macroscopic xs for molecules clarification
Example: Microscopic cross-section of H and O is and respectively. Calculate macroscopic cross-section of .
The macroscopic cross-section of a mixture is
For water, we have two atoms of H and one atom of O per one molecule of water.
Then,
Note: Here we want to calculate cross-section of a molecule. So here, will be the number of respective atoms in that molecule and N will be 1.
For example, will have a composite cross-section of and so on.

## Slide 4: Enriched uranium…again
Natural U contains ~0.7% U-235 and ~99.3% U-238 (atomic).
We do not use natural uranium in most nuclear systems. We often customize fuel such that the atomic fraction of U-235 is modified. This process is called enrichment.
Atomic enrichment: The ratio of U-235 atoms to total number of U atoms.
Mass (or weight) enrichment:
Homework (10 points): Show that . What is atomic enrichment if mass enrichment is 20%?

## Slide 5: Example
Calculate macroscopic cross-section of 8% enriched (atomic) mixed in a 1:3 volume ratio with graphite (carbon).
Okay so lets look at the problem. We have where U is 8% enriched. Moreover that is then mixed with C in a volume ratio of 1:3. So lets do this step-by-step.
Steps: Start from what you want. You want macroscopic xs of a 1:3 volume ratio mixture. Which means you use
We have two species in the mixture: and C. Therefore,
The volume fraction is 1:3 so there are 4 parts. Fractions will be ¼ and ¾ . Therefore .
Now we have new unks - and . Here use the formulas we have in the right hand column as shown in the next slide.
Once we have both macroscopic cross-sections, we can calculate what we want to calculate.

## Slide 6
Start by calculating composite microscopic xs (cross-section henceforth):
Start by calculating atomic weight of
Now calculate macroscopic xs:
Graphite
Now calculate the combined macroscopic cross-section of the mixture:

## Slide 7: Homework

## Slide 8: Reaction types
Thus far we have considered the possibility of collision and the xs that characterizes that possibility is the total xs,
A neutron that collides with nucleus can either be absorbed or scattered.
Absorption ( and scattering ( xs characterize neutron absorption and scattering respectively such that
Given a collision, the probability that a neutron will be scattered will be
Moreover, the probability that a neutron will be absorbed will be

## Slide 9: Reaction types continued
Scattering process can be broken down into elastic (KE and momentum are conserved) and inelastic (momentum conserved, KE not …some energy of neutron given to nucleus). They are denoted by and respectively.
Absorption can be broken down into capture ( and fission ( where
The total xs is then
Macroscopic xs are
Moreover,

## Slide 10: Neutron energy range
We have discussed in general about xs so far. Now let’s get a little more specific about what these interaction xs depend on.
Neutrons with different kinetic energy interact with the same material differently. We will talk about why a little later but for now let’s look at what kind of energies neutrons may be born with and what energy ranges they might slow down to due to aging - “thermalization”.
Neutrons in fission are distributed over a spectrum of energy. If we let be the fraction of fission neutrons born with energies between and , fission spectrum can be approximated using:
E is in MeV and is normalized to unity.
The logarithmic plot on the right shows fission spectrum.
Most neutrons are born in the fission energy range. Average energy is about 2 MeV and most probable energy is about 0.75 MeV.
Very few neutrons are produced above 10 MeV. Therefore, we set that as the upper limit of neutron energy range.

## Slide 11: Neutron energy range continued
We saw what energy spectrum of baby neutrons looks like. Let’s look at energies of old neutrons.
As everyone knows, when we age, we sorta get weaker…unless we’re Goku. Neutron ain’t Goku.
So as neutrons age (due successive scattering events), they lose momentum and energy to the nuclei they collide with.
At temperatures above absolute zero, nuclei possess random thermal motions and will possess a mean kinetic energy of where is Boltzmann constant and T is temperature.
In idealized situations, where there is no absorption, neutrons eventually come into equilibrium with surrounding nuclei and their energy distribution then takes the form of Maxwell-Boltzmann distribution:
Here, E is in eV. Maxwell-Boltzmann distribution is normalized to unity:
In real world, however, there is almost always some absorption, and spectrum is shifted upward form . Absorption precludes equilibrium to be established completely.
The fraction of neutrons with energies less than 0.001 eV is extremely small and this defines our lower bound of neutron energy range.
The primary range of interest is then 0.001 eV to 10 MeV.
Ranges: Thermal: 0.001 eV to 1 eV; Epithermal: 1 eV to 0.1 MeV; Fast: 0.1 MeV to 10 MeV

## Slide 12: XS energy dependence
Let’s begin with the simplest nuclide – H.
H has only one proton and therefore no internal structure and so no inelastic scattering. We will talk about inelastic scattering a little later.
It only has elastic scattering and absorption cross-sections.
The capture (absorption) xs is inversely proportional to , which in turn is proportional to . This is often referred to as xs. Only matters in thermal energy range.
where is evaluated at room temperature to be 0.0253 eV.
Total xs is
D (H-2) has similar xs except scattering xs is a little higher and absorption is much smaller (so is much better for moderation than – CANDU uses this)
Potential scattering: Similar to billiard ball collision in which KE of neutrons is conserved.
Neutrons scatter from the surface of nuclei without actually entering the interior.
Energy independent except at very low energies or high energies.
Magnitude is proportional to size of nucleus with

## Slide 13: Compound nucleus formation
If a neutron enters a nucleus instead of scattering from its surface as in potential scattering, compound nucleus is formed and it is in an excited state.
There are two contributions to this excitation energy – kinetic energy of neutron ( and binding energy . Therefore, excitation energy of compound nucleus will be (this will be true because if we assume nuclei to be at rest then the kinetic energy of the compound nucleus comes from kinetic energy of neutron itself).
Sometimes itself may amount to values in MeV. So even thermal neutrons that do not carry too much kinetic energy are capable of exciting nuclei.
Now what this influx of excitation energy will do to the nucleus depends largely on the internal structure of the nucleus.
This can be roughly understood by comparing it to structure of an atom. Electrons surrounding nucleus are in distinct quantum states and can be excited by imparting external energy.
Similarly, configurations of nucleons form nucleus are in distinct quantum states.
The addition of neutron to such nuclei creates a compound nucleus which is in an excited state due to the external energy neutron brings in.
Following the formation of compound nucleus, either the nucleus reemits the neutron returning to ground state (elastic scatter) or it will reemit a lower energy neutron and photon (inelastic scatter) to return to ground state or it will return to ground state by emitting photon/s and keep the neutron (radiative capture) or it may return to ground state by fissioning or undergo other reactions.

## Slide 14: Resonance cross-section
The likelihood of compound nucleus formation increases greatly if excitation energy incoming neutron corresponds to a quantum state of resulting nuclei.
Scattering and absorption exhibit resonance peaks at neutron kinetic energies corresponding to quantum states.
Each nuclide has its own resonance structure but in general, the heavier the nucleus, the more closely packed the quantum states will be. Sometimes the become so tightly packed that it becomes very difficult to separate them experientially and statistical theory must be used to aid in resolving them.
According to nuclear theory, energy dependence of cross-sections in vicinity of each resonance will take form of Breit-Wigner formulas.
Capture:
is the resonance energy, is width of resonance at half of xs’s max value, is radiative line width characterizing probability that the compound nucleus will decay with a gamma emission.
The adjoining figure shows absorption cross-section of U-238 as a function of energy.
Similar formula exists for scattering resonances also.

## Slide 15: Doppler broadening
Neutron cross-sections are written in terms of relative speed between neutron and nucleus in center of mass system.
Usually the neutron KE is much higher than that of nuclei due to thermal motion.
So most formulas ignore thermal motion and assume nuclei to be stationary.
If the xs is relatively smooth function of energy, the motion is unimportant.
But as we know there are resonances where xs spike and are no longer smooth.
In order to smoothen these xs curves, we average Breit-Wigner formulas over range of relative speeds as characterized by Maxwell-Boltzmann distribution of atom velocities.
This averaging smears resonance energy, making xs appear less peaked.
Smearing is more pronounced at high temperatures.
This idea is important for reactivity control that we may look at in future.

## Slide 16: Threshold cross-section
This class of reactions require a minimum KE.
As the neutron KE increases, it brings in higher excitation energy.
This means more can happen with the energy that comes in.
Some reactions do not happen unless neutrons come in at a certain “threshold” energy.
Inelastic scattering, (n,2n) reactions etc. fall under this category.
Fission reaction for fertile nuclides (e.g. U-238) is also a threshold reaction.
Adjoining figure is for U-238.

## Slide 17: Next time
Finish up Ch. 2
Review
HW-1 problems