## Slide 1: AME 480/580 Introduction to Nuclear Engineering
Transport Basics
2/23/18

## Slide 2: References
Transport Theory by Duderstadt and Martin (Ch. 1)

## Slide 3: What is Transport Theory?
Mathematical description of transport of particles through ambient medium constitutes transport theory.
Examples:
  Transport of neutrons in reactors
  Transport of light particles through atmosphere
  Motion of gas molecules as they stream and collide with one another
  Diffusion of holes and electrons in semi-conductors
  Transport of vehicles on roads
  Etc.

## Slide 4: Some Applications
Nuclear reactors
  Determination of neutron distribution in reactors
  Shielding against neutron and gamma radiation
Astrophysics
  Diffusion of light through stellar atmospheres (radiative transfer_
  Penetration of light through planetary atmospheres
Charged particle transport
  Radiation therapy (to treat tumors and cancer)
Plasma physics
  Fusion reactor dynamics (Will Taitano will talk about this next week)
Phonon transport
  Heat transport at small length scales (I will try to get someone to talk about this…no promises though)

## Slide 5: More Applications
Rarefied gas dynamics
  Upper atmosphere physics
  Diffusion of molecules in gases
Transport of electromagnetic radiation
  X-ray machines
  Multiple scattering of radar waves in turbulent atmospheres
Random walk of freshmen trying to find their first class
  Think of particles as clueless freshmen trying to find their first class. They don’t know where they are going. They go wherever people tell them to go. They go from one place to another in search of their class.
    When they reach their class – they’re “absorbed”
    When douchebag seniors bounce them from one place to another – they’re “scattered”
    When they get sick of not being able to find their class, they go home – they “leak out” of “system” called college campus
    These three phenomena largely describe transport
    Motion is assumed to be random – you never really know people and how they will behave…right?

## Slide 6: Transport vs. Continuum Description
Most macroscopic fields of interest in physics have continuum (continuous mass as opposed to discrete particles) description
  Electromagnetics – current and current densities
  Hydrodynamics – mass density, flow velocity, temperature
In transport theory, we do not have this certainty due to random nature of particle interactions. We must introduce probability density functions.
  We can only predict “expected” behavior particles and not the exact behavior of particles in a given region at a given time
What do we mean?
  There are a bunch of particles and they are all moving randomly in a medium
  Medium has its properties and particles have their own properties
  Based on these properties an “on-an-average” behavior of particles emerges
  This “on-an-average” behavior of particles is what we wish to model
  However, we are still modeling behavior of discrete particles and not a continuous medium

## Slide 7: Types of Problems in Transport
  Direct Problems
    Given – Composition and geometry of host medium; location and magnitude of sources
    Need to find – Distribution of particles in medium
    Examples – Nuclear reactor core, gas dynamics, plasma kinetics
  Inverse Problems
    Given – Distribution of particles
    Need to find – Properties of medium or sources
    Examples – Astrophysics – inferring properties of stars; nuclear medicine – diagnosing cancer/tumors etc.; detection of nuclear materials at ports; stuff Kyle talked about last class

## Slide 8: Characterizing Particle Motion
  Expected particle density: Expected (on-an-average) number of particles in a differential physical volume about at time :
  The knowledge of expected particle density is sufficient for most applications but no known equation adequately describes that for most practical situations.
  The concept of expected particle density must be generalized to account for more independent variables to characterize particle motion.
  We now characterize the state of a particle using particle position, , and velocity, We introduce phase-space density function (next slide).
  Position and velocity are adequately describe motion of neutrons, photons, molecules, phonons etc.

## Slide 9: Phase-Space Density Function
  Particle position and velocity constitute phase-space of the density function. We define phase-space density function as:
  – expected number of particles in differential volume about position with velocity about velocity at time .
  This function contains all the information required to describe transport processes. We can integrate this function over velocity to obtain expected particle density:
  In kinetic theory, phase-space density function is normalized by expected particle density to obtain probability distribution or density function:
  Where,

## Slide 10: Decompose Velocity Vector
  Velocity vector is decomposed into – speed and direction
  Speed:
    Often, kinetic energy, is used to represent speed.
  Direction:
    We introduce unit vector (in spherical velocity coordinates)

## Slide 11: Phase-Space Density Function - Rewritten
  Now we rewrite the phase-space density function in terms of kinetic energy and direction:
  - Expected number of particles in differential volume about position with kinetic energy in moving in direction in solid angle
  The expected particle density can be written as:
  Where,

## Slide 12: Angular Current Density
Expected number of particles with kinetic energy in moving in direction in solid angle that cross an area per second:
Where, . is the rate at which particles pass through a differential surface area .

## Slide 13: Partial Currents
The rate at which particles flow through an area in a given direction is characterized through partial currents:
is the unit normal to the surface. The integral over velocities is only taken over those particles directions in the positive or negative directions. The net current density is:
Notice angle-dependent quantities are lower-case and angle-integrated quantities are upper-case.

## Slide 14: Derivation of generic transport equation – Volume of Interest
Consider an arbitrary volume, V. We wish to calculate the time rate of change of number of particles in this volume with velocity in about
We ignore macroscopic forces that may affect particle motion in volume V.

## Slide 15: Generic Balance Equation
Leakage through S; Changes due to collision; Sources
Each term is expressed mathematically, manipulated in various ways based on different physics and we get different transport equations through the above balance equation. We have the following generic balance equation.

## Slide 16: The balance equation
+ =
Rate of change
leakage
Long range forces
Total removal due
to collision
Total inscatter
source

## Slide 17: Angular flux (aka phase space flux) and scalar flux
We define angular flux as
– total rate at which particles of a given velocity pass through a given unit surface area.
Scalar flux is the velocity integrated flux:
- is the total rate at which particles (of all velocities) pass through a given unit area regardless of orientation.
Angular flux and angular current density are related as:

## Slide 18: The Transport Equation
If we write everything in terms of the definitions of angular flux and write velocity as energy and angle of motion, our balance equation (ignoring long range forces):
+ =
becomes:
=

## Slide 19: How do we solve this Fugly?
As one can imagine, the transport equation we see on the previous slide can depend on 7 independent variables – 3 space, 2 direction, one energy, and time. The equation is 7D.
So people choose two different ways from here:
  Solve the transport equation itself – Discretize the equation in space (finite element, finite volume, finite difference etc.), direction (discrete ordinates, expansion in spherical harmonics etc.), energy (multigroup), and time (backward Euler, Runge-Kutta etc.).
  Approximate the transport equation using various mathematical methods (asymptotics, moments etc.) that are valid for specific regimes – diffusion equation, equations, equations, Fokker-Planck equation etc.
Both ways usually require us to solve a matrix equation. How easy it is to setup the matrix equation depends on what level refinement we want in our solution.
How easy it is to solve the matrix equation depends on the largest eigenvalue (in terms of magnitude) of the coefficient matrix (spectral radius).
More advanced solution techniques incorporate parallel solves and preconditioning.
Acceleration techniques can be either linear or nonlinear (we can talk about this later in the course if we have time…maybe if my advisor decides to give a talk I’ll ask him to talk on this…if he doesn’t do it, I’ll call myself to do a guest lecture…it will be your pleasure to listen to me one more time lol).